## Slide 1
UART with Classification Engine
ECGR 4146/5146 — Introduction to VHDL | Spring 2026
Group Members: Alberto Hernandez · Kenneth Le · Erik Contreras Valdivia · Sebastian Navarro
April 30, 2026

## Slide 2
Overall System Architecture
Serial
Input
RX line
idle HIGH
UART
Receiver
4-state FSM
16× oversample
RX
FIFO
16 entries
8-bit wide
FSM
Controller
FIFO→RAM
byte packing
Block
RAM
32×32-bit
sync read
Classifier
6-state FSM
byte class
TX
FIFO
255 slots
buffers results
UART
Transmitter
4-state FSM
LSB-first
Baud Rate Gen
651 div · 16× OVS
phase = 0 (receive): FSM owns RAM address | phase = 1 (classify): engine owns RAM address
100 MHz clk · 9600 baud · 8N1 · LSB-first · Active-HIGH reset

## Slide 3
Baud Rate Generator
baud_gen.vhd
Module Diagram
Counter
0 → M−1
(M = 651)
clk
tick
count = M−1?
YES → tick='1', count→0
NO → count+1
Clock
100 MHz
Baud rate
9600 bps
Oversample
16×
Divisor M
651 cycles
Tick period
~6.51 µs
Tick width
1 clock cycle

## Slide 4
UART Receiver
uart_rx.vhd
IDLE
START
DATA
STOP
rx='0'
s_tick,
s_cnt=7
s_tick,
n_cnt=7
SB_TICK done → rx_done='1'
How it works
Wait for RX to go LOW (start bit detected)
Skip 7 ticks to center-align on start bit
Sample RX at tick 15 (mid-bit) for each data bit
Shift bits in LSB-first via 8-bit shift register
Wait stop bit duration → assert rx_done for 1 cycle
Key signals
s_tick — 16× baud tick from baud_gen
rx_done — 1-cycle pulse when byte is ready
dout — received byte, stable until next frame
SB_TICK = 16 (one stop bit at 16 ticks per bit)

## Slide 5
UART Transmitter
uart_tx.vhd
IDLE
1
START
0
D0=1
1
D1=0
0
D2=1
1
D3=0
0
D4=1
1
D5=0
0
D6=1
1
D7=0
0
STOP
1
TX Line — example byte 0x55 (01010101), LSB-first
IDLE
START
DATA
STOP
Transmission flow
IDLE: tx='1', waits for tx_start='1'
START: drives tx='0' for 16 ticks (1 bit period)
DATA: shifts out 8 bits LSB-first at 16 ticks/bit
STOP: drives tx='1' for SB_TICK ticks
Asserts tx_done for 1 cycle, returns to IDLE
Design details
Separate state & datapath registers for clean FSM style
b_reg holds byte; shifts right to expose next LSB
s_reg counts ticks 0–15 within each bit period
n_reg counts data bits sent (0–7)
tx_done registered to avoid glitches

## Slide 6
FIFO Buffer
fifo.vhd
Circular
Buffer
wr + w_data →
→ r_data
rx_fifo (RX path)
Depth: 16 entries (ADDR_W=4)
wr ← rx_done from uart_rx
rd ← fifo_rd from uart_fsm
Decouples serial RX from FSM
tx_fifo (TX path)
Depth: 255 entries (ADDR_W=8)
wr ← result_valid from classifier
rd ← TX controller FSM
Buffers all 128 results at once
Full / Empty logic
empty = '1' when w_ptr = r_ptr (no data)
full = '1' when ptr_inc(w_ptr) = r_ptr (one slot reserved)
Simultaneous rd+wr allowed — write permitted if rd happening
Prevents ambiguity between full and empty states
FWFT behavior: r_data valid while empty='0' (no extra rd strobe)

## Slide 7
RAM Module & FSM Controller
RAM Module — ram_module.vhd
32-bit wide × 32-row synchronous block RAM
Synchronous write: din → ram(addr) on rising edge when we='1'
Synchronous read: 1-cycle latency (dout registered)
Inferred as Xilinx BRAM in synthesis
Shared by FSM (write) and classifier (read) via mux
FSM Controller — uart_fsm.vhd
IDLE → READ_BYTE → PACK → WRITE_RAM → DONE_PULSE → DONE
Reads one byte per state from FWFT FIFO
Packs 4 bytes into 32-bit word (little-endian)
Writes word to RAM every 4 bytes received
Pulses fsm_done after row 31 is written
Byte packing — little-endian:
[31:24]
byte3
[23:16]
byte2
[15:8]
byte1
[7:0]
byte0
byte0 = first received ← byte3 = fourth received

## Slide 8
Classification Engine
classification_engine.vhd
0x01
Uppercase
A–Z (0x41–0x5A)
0x02
Lowercase
a–z (0x61–0x7A)
0x03
Digit
0–9 (0x30–0x39)
0x00
Other
anything else
IDLE
READ_ADDR
WAIT_RAM
CLASSIFY
OUTPUT
DONE_ST
How it works
Triggered by fsm_done pulse; reads RAM addresses 0–31 in sequence
WAIT_RAM state absorbs the 1-cycle registered read latency
CLASSIFY: runs classify_byte() on all 4 byte lanes of the 32-bit word simultaneously
OUTPUT: streams 4 results one per cycle via result + result_valid; then advances to next row
Asserts done for 1 cycle after all 32 rows processed; returns to IDLE

## Slide 9
System Integration & Top-Level Testbench
uart_top.vhd — key design choices
Phase register: 0=receive, 1=classify; controls RAM addr mux
TX controller: 3-state FSM drains TX FIFO one byte at a time
TX FIFO (255 deep) absorbs all 128 results while TX runs at 9600 baud
All modules share one baud_gen tick, no clock domain issues
tb_uart_top.vhd — integration testbench
Sends 128 bytes: ABcd1234EFgh5678 + 112 null bytes via RX
Concurrently samples TX line, aligns to center of each bit
Checks all 128 classification codes byte-by-byte
Reports pass/fail summary with hex values per byte
Expected classification results for typed bytes:
Char | Hex in | Expected out | Class
A B | 0x41 0x42 | 0x01 0x01 | Uppercase
c d | 0x63 0x64 | 0x02 0x02 | Lowercase
1 2 3 4 | 0x31–0x34 | 0x03 ×4 | Digit
E F | 0x45 0x46 | 0x01 0x01 | Uppercase
g h | 0x67 0x68 | 0x02 0x02 | Lowercase
5 6 7 8 | 0x35–0x38 | 0x03 ×4 | Digit
null ×112 | 0x00 ×112 | 0x00 ×112 | Other

## Slide 10
Challenges & Solutions
FIFO Full/Empty Ambiguity
Both states result in w_ptr = r_ptr. Solution: reserve one slot full when ptr_inc(w_ptr) = r_ptr, empty when w_ptr = r_ptr.
FIFO Read Latency in FSM
fifo_dout changes one cycle after fifo_rd pulses. FSM latches the byte into byte_buf in READ_BYTE before advancing pointer, then packs from byte_buf in PACK.
RAM Address Mux
FSM (write) and classifier (read) both need RAM addr. Solution: phase register switches ownership after fsm_done/ce_done clean and transparent to both modules.
TX FIFO Depth
Classifier produces 128 results faster than 9600-baud TX can drain them. TX FIFO sized to 255 entries (ADDR_W=8) to buffer all results in one shot.

## Slide 11
Challenges & Solutions
Clock Dependency in Synchronous RAM
During RAM verification, the output (dout) remained undefined (U) despite valid input signals (we, din, addr). This issue was traced back to the absence of a proper clock signal in the testbench. Since the RAM uses synchronous read/write operations, no data transfers without a clock edge. The problem was resolved by implementing a clock generation process in the testbench, which introduces periodic rising edges and enabled correct write and read behavior. After this fix, the output updated as expected, confirming proper functionality of RAM module.
Testbench Inconsistency Across Modules
A testbench that initially ran correctly for one module failed when reused or adapted for other modules during integration. This was due to mismatches in signal timing, initialization, and stimulus assumptions between modules. The issue was resolved by standardizing testbench structure, carefully aligning timing (e.g., clock/reset behavior and control pulses), and verifying each module interface requirements before integration.
One Cycle Read Latency in RAM
While testing the RAM module, it initially appear that the output (dout) was incorrect because it did not immediately reflect the newly written data. Instead, the output showed the previous value during the same clock cycle as the write operation. This behavior was identified as expected due to the synchronous read design, where data is only available one clock cycle after being written. By analyzing the waveform across multiple clock cycles, the correct timing relationship was confirmed, verifying that the RAM module was functioning as intended.
AI Tool Usage
Helped identify a subtle timing issue in the FSM, specifically that fifo_dout would already reflect the next byte by the time the PACK state executed, which led to the byte_buf latching fix in READ_BYTE. Second, it was used to draft and maintain INTERFACE_AGREEMENT.md, which served as the team's shared reference for port names, signal widths, and active levels across all modules. Third, it was used to review VHDL modules and testbenches for correctness and consistency.

## Slide 12
Results & Verification
8
VHDL modules
9
Testbenches
128
TX bytes verified
32
RAM rows packed
9600
Baud rate
baud_gen
✓ Tick period 6.51 µs verified
uart_rx
✓ 4 byte patterns all pass
uart_tx
✓ 2 byte patterns serial output correct
fifo
✓ 8 test cases incl. full/empty/sim-rw
ram
✓ Write, readback, overwrite all pass
uart_fsm
✓ 3 RAM words verified (rows 0,1,31)
classifier
✓ 128/128 results correct incl. boundaries
uart_top
✓ Full end-to-end integration all 128 TX bytes match

## Slide 13
Conclusion
Complete UART subsystem verified from baud_gen to end-to-end TX output
FSM-driven FIFO→RAM packing with little-endian byte ordering
Classification engine categorizes all 128 bytes correctly at full simulation speed
Phase-based RAM arbitration keeps FSM and classifier fully decoupled
All modules verified with individual testbenches, full system integration passes 128/128 TX byte check
ECGR 4146/5146 — Spring 2026 | Alberto · Kenneth · Erik · Sebastian